## Slide 1: CSE 141: Introduction to Computer Architecture
Pat Pannuto, UC San Diego
Human Perception
Camera Perception
ppannuto@ucsd.edu

## Slide 2: What is Computer Architecture and where does it fit in Computer (Science) Engineering?
One view: what is an Architect and how do they fit in the creation of buildings?
Zaha Hadid
Port Authority Building in Antwerp, designed by Zaha
Graphics courtesy Wikipedia
Notes: Idea: architects responsible for the design, pulling all the pieces together, high-level vision

## Slide 3: Computer science is all about abstractions
Chip Fabrication
Physical Layout (VLSI)
Digital Logic / Circuits
Computational Units
Processor
Operating System
Programming Language / Runtime
Applications
The person who designs this…
…only needs to worry about these
But who designs the big picture?

## Slide 4: Computer architects look at the system as a whole and design abstractions
Chip Fabrication
Physical Layout (VLSI)
Digital Logic / Circuits
Computational Units
Processor
Operating System
Programming Language / Runtime
Applications
Instruction Set Architecture
Machine Organization
Arithmetic & Number Systems
CSE 141
Notes: Idea, the orange boxes exist as layers because architects described how to effectively decompose systems
-- echo and amplify H&P’s tenet: “Use Abstractions to Simplify Design”
This class focuses on the classic foundations of arch: [top-down] how does software talk to hardware, [bottom-up] how to turn digital logic into computable elements, [put it together] how to best put these pieces together

## Slide 5: Good abstractions make it easier to focus on reasoning about one part of a large, complex system
Which of these maps is easier to use to plan a trolley trip?
Notes: What is an abstraction?

## Slide 6: Good abstractions make it easier to focus on reasoning about one part of a large, complex system
Modularization is fundamental to design in many domains
https://www.reddit.com/r/dataisbeautiful/comments/8m15g9/automobile_platform_sharing_work_in_progress/
Modular Car Body Design and Optimization by an Implicit Parameterization Technique via SFE CONCEPT
Fabien Duddeck, Hans Zimmer
Notes: What is an abstraction?

## Slide 7: But what if I’m not going to become a computer architect?
Chip Fabrication
Physical Layout (VLSI)
Digital Logic / Circuits
Computational Units
Processor
Operating System
Programming Language / Runtime
Applications
If I only want to build these…
…why do I need to know
about any of this?

## Slide 8: The real world is full of leaky abstractions
Goal: Sum up all the entries of a two dimensional array
Which of these implementations is faster?
int twoDarray[256][256];
int sum = 0;
for (int i=0; i<256; i++) {
for (int j=0; j<256; j++) {
sum += twoDarray[i][j];
}
}
int twoDarray[256][256];
int sum = 0;
for (int i=0; i<256; i++) {
for (int j=0; j<256; j++) {
sum += twoDarray[j][i];
}
}
Answer: “It depends”

## Slide 9: Architects look across systems to find and improve inefficiencies – always valuable, sometimes critical…
What happens when workload changes overnight, and there’s no way to buy your way out of the problem?
  Architects help to fix it

## Slide 10: Course Administrivia
Instructors
  Sec A00: Pat Pannuto
  Sec B00: Dean Tullsen
The sections will run “in sync”
  We will have shared assignments, shared exams
  The lectures will cover the same content but in different ways
    You may watch either lecture (or both!)
    If something I say is confusing, maybe watching Dean will help (or vice-versa)

## Slide 11: Course Staff
Four amazing TAs:
  Kazem Taram
  Nitish Kulshrestha
  Shanti Modi
  Sumiran Shubhi

## Slide 12: Assessments & Workload
Grading
  Participation: 10%
    Weekly participation quizzes of lecture material (10 weeks -> 1% / quiz!)
  Homework: 15%
  Midterm: 30%
  Final Exam: 45%
    (Inclusive final)
    Our assigned final exam slot is SATURDAY, December 12 — Plan for this now!
Workload
Academic Integrity

## Slide 13: Active engagement is key to effective learning
Watching videos is not a passive activity
  Write down questions about what you do not understand!
  Use checkpoints effectively
  Watching (or reading) 5 minutes before class is better than not at all, but 5+ hours before is much better
Lectures, office hours, and exercises are not passive activities
  Work through examples and ask the questions you have
Homework is designed to help you solidify your understanding
Study for tests “honestly to yourself” – you must engage with questions

## Slide 14: And then some modern highlights from here at ucsd
We’ll take a 3-5 minute break here…

## Slide 15: This class will build up architecture from the fundamentals
Video 1, Slide 1:

## Slide 16: But for the rest of today, I want to highlight the kinds of cool stuff that architects do
UCSD has an amazing team of architecture faculty

## Slide 18
Notes: “Alternative Computing Technologies”
Look at how ideas are inter-related; approx. comp will evolve from

## Slide 19: One wild idea: “Approximate Computing”
Aka, what if 1 + 1 doesn’t always equal exactly 2?

## Slide 20: Embracing imprecision allows for major gains in performance and energy
IoT
Mobile
Desktop
Data center
Imprecision

## Slide 21
Techniques
Quality Control
End-users
Apps
Language
Compiler
Arch
Microarch
Circuit
Devices
NPU
[MICRO‘12]
ANPU
[ISCA‘14]
SNNAP
[HPCA’15]
NGPU
[MICRO’15]
AxRAM
[PACT’18]
FLEXJAVA
[FSE‘15]
AXBENCH
[IEEE D&T’16]
TRUFFLE
[ASPLOS‘12]
AXILOG
[DATE’15, IEEE Micro’15]
AXGAMES
[ASPLOS’16]
MITHRA
[ISCA’16]
RFVP
[PACT’14, IEEE D&T’15, ACM TACO’16, HiPEAC’16]
GRATER
[DATE’16]
A cross-stack approach to enable approximation

## Slide 22: Privacy Preserving Techniques for Inference
Accuracy Loss
Privacy
Accuracy-Agnostic
Noise Addition
Computation Cost
Homomorphic Encryption
Shredder
Notes: Conceptually, if we want to achieve higher privacy on a pretrained model using noise naively, we would incur huge amounts of accuracy loss. Another method to achieve privacy for inference is HE, which is extremely compute intensive and Adds computing overhead to both server- and edge-sides. This is particularly concerning for the edge devices that are resource constrained.
We propose shredder, which learns noise distributions that are tolerated by the network and do not harm accuracy, while decreasing the amount of excessive information in the input.

## Slide 23: Execution Model
Previously Trained Noise Distributions
+
Sent to the Cloud
Notes: Our execution model consists of splitting the neural network into 2 parts, and executing the first part on the edge device, and the second more compute intensive part on the cloud. To increase the privacy of the edge device, we add our randomly generated calibrated noise to the output of the edge partiontion, which obfuscate the excessive information, while maintaining the accuracy.

## Slide 24: Rethinking the abstractions
Physical Device
Circuit
Architecutre
Compiler
Programming Language
Algorithms
Microarchitecture
Precision
Generality
Efficiency
Performance
Cost
Cost

## Slide 25: Memory, Storage, Software, and Architecture in the NVSL

## Slide 26: This is a slide you will encounter in many CE/CSE classes…
Chellappa, Srinivas & Franchetti, Franz & Püschel, Markus. (2007). How to Write Fast Numerical Code: A Small Introduction.
Non-Volatile Memory
Notes: Traditional data hierarchy
NVM messes with this because it’s almost as bit has hard drives but as fast as main memory – how does that change the rest of the computing system?

## Slide 27
Hardware
Applications
Tools
Libraries
Languages
Operating Systems
Distributed Systems
MARS
Willow
QuickSAN
Moneta
NV-Heaps
Pangolin
Pronto
NOVA
Orion
Ziggurat
SubZero

## Slide 28: NVSL Students Lead Industry
We Built
  Opt. SSD interface (2009)
  Direct, remote SSD (2013)
  First PCM SSD (2011)
  PMEM prog. tools (2011)
Industry Built
  NVMe (2011)
  NVMe over Fabrics (2016)
  Optane (2016)
  PMDK (~2014)

## Slide 29: Mobilizing the Micro-Ops: Exploiting Context Sensitive Decoding for Security and Energy Efficiency

## Slide 30: Leaky abstractions are not always just performance problems…
This loop behaved differently because of how caches work
Architects added “hidden” caches: faster, intermediate memories

## Slide 31: Leaky abstractions can be security threats!
Notes: When things behave differently (that should not have) on shared machines (i.e. the cloud) – you can steal data!

## Slide 32: Mobilizing the Micro-Ops Exploiting Translated ISAs
Instruction Decoder
Fetch
Rename
Execute
WB
5
Notes: This is a simple pipeline, which is at the heart of every processor; we’ll learn about this in class

## Slide 33: Mobilizing the Micro-Ops Exploiting Translated ISAs
Native Instructions (e.g., inc [0x803ac] )
Instruction Decoder
Fetch
Rename
Execute
WB
5

## Slide 34: Mobilizing the Micro-Ops Exploiting Translated ISAs
Native Instructions (e.g., inc [0x803ac] )
Instruction Decoder
Fetch
Rename
Execute
WB
ld t0, [0x803ac]
add, t0, t0, 1
st [0x803ac], t0
5

## Slide 35: Mobilizing the Micro-Ops Exploiting Translated ISAs
Native Instructions (e.g., inc [0x803ac] )
Instruction Decoder
Fetch
Rename
Execute
WB
ld t0, [0x803ac]
security_check1
add, t0, t0, 1
security_check2
st [0x803ac], t0
5

## Slide 36: Context Sensitive Decoding fixes a leaky abstraction
Eliminating cache side channels via cache obfuscation
Energy and Performance optimization via selective devectorization
  ISCA 2018
  IEEE Micro Top Picks in Computer Architecture
Spectre mitigation via targeted insertion of fence micro-ops (Context Sensitive Fencing)
  ASPLOS 2019
Notes: Hadi and Steve examples were architecture that makes changes across the whole stack
Dean example makes changes at a very targeted point to make promises across the stack hold true again

## Slide 37: Performance was king, until we unplugged computers
A lot of architecture research is about making sure graphs continue to go up and to the right

## Slide 38: I spend my time on graphs that go down and to the right
Mini Computer
Laptop
Workstation
Personal Computer
Mainframe
Smartphone
IoT/Wearable
With the laptop class, computing “cut the cord” and energy (battery life) became a first-class concern
Computer
Battery
By volume, the emerging computing classes are mostly energy storage
Volume is shrinking cubically
Notes: Defining feature of modern computing classes is the amount of energy storage required to allow their operation
Clip art: http://www.ctecsolar.com/cut-cord-electric-company/
X-rays: iFixit teardowns

## Slide 39: Computational platforms will continue to scale
Mini Computer
Laptop
Workstation
Personal Computer
Mainframe
Smartphone
IoT/Wearable
The next generation of computing will only be a cubic millimeter in size
“Smart Dust”
Millimeter-scale batteries have capacities around 5 µAh
(would power an idle iPhone for 0.6 s)
Notes: Clip art: http://www.ctecsolar.com/cut-cord-electric-company/
X-rays: iFixit teardowns
Watch: 291.8e-3 / 5e-6 = 58360
Phone: 2659e-3 / 5e-6 = 531800
Not the greatest paper, but maybe a reasonable estimate of actual power draw of iphone 5s: https://arxiv.org/pdf/1606.05576.pdf
1560 mAh / 51.27h = 0.0305 A
(.005 mAh) / (0.03046875 amperes) = 0.590769231 seconds

## Slide 40: Energy constraints will play a central role in the evolution of computing platforms
Mini Computer
Laptop
Workstation
Personal Computer
Mainframe
Smartphone
IoT/Wearable
“Smart Dust”
How must traditional paradigms change, adapt, or re-invent for the new computing classes?
Notes: Clip art: http://www.ctecsolar.com/cut-cord-electric-company/
X-rays: iFixit teardowns
Watch: 291.8e-3 / 5e-6 = 58360
Phone: 2659e-3 / 5e-6 = 531800

## Slide 41: One of the first challenges was re-thinking how we put together computers
Temperature Sensor
~10 pW standby, < 1 µW active
CPU
~1 nW standby, ~5 µW active
Radio
~10 pW standby, ~10 µW active
Energy Harvesting & Storage
1~10 nW indoors
2~10 µAh capacity
?

## Slide 42: MBus enabled the of development of dozens of millimeter-scale motes as part of the Michigan Micro Mote (M3) project

## Slide 43: Check out the “World’s Smallest Computer” exhibit at Silicon Valley’s Computer History Museum!